## Slide 1: Sniffing

## Slide 2: Introduction
Sniffing is passively eavesdropping on the network.
A way for hackers to gain information on the network. E.g.
  Username and password
  Message
  Visiting website
Can also be used as an investigating technique.

## Slide 3: Local Area Network (LAN)
Computers and network devices are interconnected by a shared transmission medium.
Cabling system
  Copper twisted-pair cable (e.g., Cat5E/6/7/8)
  Optical fiber

## Slide 4
Network devices
  Hub / Switch
    Create a network by connecting the computers together
  Router
    Connect two networks together (e.g. LAN and WAN)
      WAN: Wide Area Network
  For a home router we use nowadays, it consists of three components
    Router, switch, and firewall

## Slide 5
Computers and network devices are connected to the cabling system through the Network Interface Card (NIC)
  Assigned with a unique Media Access Control (MAC) address hardcoded in ROM
    MAC address / Physical address / Hardware address
    Six bytes
      First three bytes specify the card vendor
      Remaining three bytes specify a unique number for that vendor.
    Most routers or operating systems nowadays allow us to change the MAC address on the software level.

## Slide 6
  Contain hardware that allows it to recognize
    Its MAC address
      Normally, NIC only accepts frames destined to its specific MAC address, and all other frames are ignored.
    Broadcast address
    Multicast addresses that direct frames to groups of stations.
  Can be set to run in the promiscuous mode where it listens to all transmissions.
    In the promiscuous mode, the NIC will accept the received frame that is not destined to it.
    Used by system administrators to troubleshoot the network.
    Used by hackers to intercept unencrypted passwords and other information.

## Slide 7: Star Topology
Hub / Switch
Image source: https://en.wikipedia.org/wiki/Star_network#/media/File:Star_Topology.png

## Slide 8
Widely used in LAN nowadays.
Connected to either a hub or a switch.
  Hub
    Repeat the incoming frames to ALL outgoing ports.
  Switch
    The incoming frames are examined and transferred to the appropriate outgoing ports only.
  In the past, the switch is much more expensive than the hub.
  Nowadays, the switch is much cheaper and the hub is rarely used.

## Slide 9
HTTP Request
TCP Header
IP Header
Frame Check Sequence
Ethernet Header
Application Layer
Transport Layer
Header contains source and destination port numbers, etc.
Internet Layer
Header contains source and destination IP addresses; transport protocol type, etc
Network Interface
Header contains source and destination MAC addresses; network protocol type, etc.
TCP/IP 4-Layer Model

## Slide 10: TCP vs. UDP
Transmission Control Protocol (TCP)
  Connection-oriented communication
  Adv: more reliable, ordered
  Disadv: heavyweight
  Example: www, email, ssh
User Datagram Protocol (UDP):
  Connectionless communication
  Adv: lightweight
  Disadv: less reliable, not ordered
  Example: Domain Name Service (DNS):
    Given a host name, lookup the IP address
Notes: Reference: http://www.cyberciti.biz/faq/key-differences-between-tcp-and-udp-protocols/

## Slide 11
socket()
bind()
listen()
read()
close()
socket()
connect()
read()
write()
close()
blocks until server receives
a connect request from client
data
data
Server
Client
accept()
write()
connect negotiation
Socket calls for connection-oriented communication
create an endpoint for communication
assign an address (IP address / port pair) to the socket

## Slide 12
socket()
bind()
sendto()
close()
socket()
bind()
recvfrom()
sendto()
close()
blocks until server
receives data from client
data
data
Server
Client
recvfrom()
(optional)
Socket calls for connectionless communication

## Slide 13: How sniffers work?
A packet sniffer is a program that eavesdrops on the network traffic.
It captures data that pass across the network.
Normal condition
  Data is placed in frames for LAN.
  Each frame is addressed to a particular MAC address.

## Slide 14
  Each network interface card (NIC) and network device has a unique MAC address.
    It is possible to change the MAC address on software level.
    But usually the network administrator will set the policy preventing the MAC address from changing.
  Normally, NIC only accepts frames destined to its specific MAC address, and all other frames are ignored.
Promiscuous mode
  When the NIC is in promiscuous mode, it will accept frames regardless of the MAC address.

## Slide 15: Writing a Simple Sniffer
socket()
bind()
Promiscuous
mode
recvfrom()

## Slide 16
Here is the code for a simple sniffer
(from Chapter 9 of “Hack proofing your network”)
Notes: #include <stdio.h>
#include <stdlib.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <netinet/in.h>
#include <linux/if_arp.h>
#include <linux/if_ether.h>
#include <linux/sockios.h>
#include <net/ethernet.h>
int open_interface(char *name)
{
struct sockaddr addr;
struct ifreq ifr;
int sockfd;
/* open a socket and bind to the specified interface*/
sockfd = socket(AF_INET, SOCK_PACKET, htons(ETH_P_ALL));
if (sockfd < 0)
return -1;
memset(&addr,0,sizeof(addr));
addr.sa_family = AF_INET;
strncpy(addr.sa_data,name,sizeof(addr.sa_data));
if (bind(sockfd,&addr,sizeof(addr)) != 0) {
close(sockfd);
return -1;
}
/* check to make sure this interface is ethernet, otherwise exit */
memset(&ifr,0,sizeof(ifr));
strncpy(ifr.ifr_name, name, sizeof(ifr.ifr_name));
if (ioctl(sockfd,SIOCGIFHWADDR,&ifr) < 0) {
close(sockfd);
return -1;
}
if (ifr.ifr_hwaddr.sa_family != ARPHRD_ETHER) {
close(sockfd);
return -1;
}
/* now we set promiscuous mode */
memset(&ifr,0,sizeof(ifr));
strncpy(ifr.ifr_name,name,sizeof(ifr.ifr_name));
if (ioctl(sockfd,SIOCGIFFLAGS,&ifr) < 0) {
close(sockfd);
return -1;
}
ifr.ifr_flags |= IFF_PROMISC;
if (ioctl(sockfd,SIOCSIFFLAGS,&ifr) < 0) {
close(sockfd);
return -1;
}
return sockfd;
}
/* read ethernet packets, printing source and destination address */
int read_loop(sockfd)
{
struct sockaddr_in from;
char buf[1792], *ptr;
int size, fromlen, c;
struct ether_header *hdr;
while (1) {
/* read the next available packet */
size = recvfrom(sockfd, buf, sizeof(buf), 0, &from, &fromlen);
if (size < 0)
return -1;
if (size < sizeof(struct ether_header))
continue;
hdr = (struct ether_header *)buf;
/* print out ethernet header */
for (c = 0; c < ETH_ALEN; c++)
printf("%s%02x",c==0 ? "" : ":",hdr->ether_shost[c]);
printf(" > ");
for (c = 0; c < ETH_ALEN; c++)
printf("%s%02x",c==0 ? "" : ":",hdr->ether_dhost[c]);
printf(" type: %i\n", hdr->ether_type);
}
}
int main(int argc, char **argv)
{
int sockfd;
char *name = argv[1];
if (!argv[1]) {
fprintf(stderr,"Please specify an interface name\n");
return -1;
}
if ((sockfd = open_interface(name)) < 0) {
fprintf(stderr,"Unable to open interface\n");
return -1;
}
if (read_loop(sockfd) < 0) {
fprintf(stderr,"Error reading packet \n");
return -1;
}
return 0;
}

## Slide 17
int socket(int family, int type, int protocol)
Create an endpoint for communication
family: identifies the family by address or protocol
  AF_INET is for IPv4 (4 bytes for an IP address)
  AF_INET6 is for IPv6 (16 bytes for an IP address)
type: identifies the semantics of communication
  SOCK_STREAM
    Sequence of bytes, does not preserve message boundary
  SOCK_DGRAM
    In blocks of bytes called datagram
  SOCK_RAW
    Access to internal network interface (superuser)
  SOCK_PACKET
    To get Ethernet packets (for Linux).

## Slide 18
protocol: identifies protocol (0 - default)
  IPPROTO_TCP
    with SOCK_STREAM and AF_INET (or AF_INET6)
  IPPROTO_UDP
    with SOCK_DGRAM and AF_INET (or AF_INET6)
  ETH_P_ALL
    Get Ethernet packets.
    In the code, htons() is used to convert to TCP/IP network byte order (big-endian)

## Slide 19
int bind(int sd, struct sockaddr *name, int namelen)
Assign an address to the socket.
sd
  the socket descriptor returned by the socket call.
name
  a pointer to an address structure.
namelen
  the size of address structure.

## Slide 20
struct sockaddr {
sa_family_t sa_family; /* address family */
char sa_data[14]; /* up to 14 bytes of direct address */
};
sa_familiy = AF_INET
sa_data = name of the interface (e.g., eth0, eth1)
In our sniffer, sockaddr is used to assign the value.
  sockaddr is a generic socket type
  But for normal network programming using IPv4, we use sockaddr_in to assign the values, which also contains the port number and the IP address

## Slide 21
ioctl operation
  Has traditionally been the system interface.
  Used by network programming to
    obtain interface information
    set the interface configuration
    access the routing table
    access the ARP cache
  Here we will use this function to
    ensure the interface is Ethernet
    set the network interface to promiscuous mode

## Slide 22
ioctl(int fd, int request, /*void *arg */);
fd
  the socket descriptor returned by the socket call.
request: type of the request
  SIOCGIFHWADDR
    Get the hardware address in the ifr_hwaddr member
  SIOCGIFFLAGS
    Get the interface flags in the ifr_flags member
  SIOCSIFFLAGS
    Set the interface flags from the ifr_flags member
arg
  address of an ifr record

## Slide 23
recvfrom(int sockfd, void *buf, size_t len, …)
  Get the next available packet and store the data into buf.

## Slide 24
We can also use libpcap to implement our sniffer.
  libpcap is an open source library for packet capturing and filtering.
More information can be found at http://www.tcpdump.org/
Wireshark (formerly Ethereal) is implemented using libpcap.
Notes: Demo on ethereal
startx  ethereal
Machines A, B, and C are connected by a hub.
A: hacker (perform sniffing)
B: telnet client (telnet to C)
C: telnet server

## Slide 25: Some Common Sniffers
Wireshark
  https://www.wireshark.org/
Snort
  http://www.snort.org
Tcpdump
  http://www.tcpdump.org

## Slide 26: What can a sniffer do?
Determine the local gateway of an unknown network via passive sniffing.
Become a simple password sniffer
  Parsing each application protocol and saving interesting formation.
    Header information.
    Username and password etc.
Output all requested URLs sniffed from HTTP traffic and analyze them offline.
Send URLs sniffed from the target to an Internet browser for display.
Notes: http demo by lynx and ethereal

## Slide 27
Common application protocols that are interested by hackers.
  telnet (port 23)
  ftp (port 21)
  pop (port 110)
  imap (port 143)
  rlogin (port 513)
  NFS files handles
  Windows authentication
  HTTP (Port 80)
  It can also watch IP, TCP, UDP, ICMP, ARP, RARP.

## Slide 28: Detection of Quiet Sniffers
Properties
  Collect data only
  Do not respond to any of the information
  Do not generate their own traffic
Requires physical checking
  Ethernet connections
  Check the configuration of network card
    E.g., ip link
    It is known that “ifconfig” may not work properly for checking the promiscuous mode

## Slide 29: Detection of Malicious Sniffer
DNS Test
  Domain Name Service (DNS)
    Given a host name, lookup the IP address
  Reverse DNS
    Given an IP address, lookup the host name
  In the DNS test, the administrator creates numerous fake TCP connections.
  Expecting a poorly written sniffer to
    Pick up on those connections.
    Resolve the IP addresses of the nonexistent hosts.
  The administrator sniffs the network to see if there is any reverse DNS lookup request looking up for the nonexistent host.
Notes: ?

## Slide 30
Ping Test
  The administrator constructs an ICMP echo request
    Set the IP address to that of the suspected host.
    Intentionally choose a mismatched MAC address.
  Most systems will ignore this packet since its MAC address is wrong.
  In some systems, if the NIC is in promiscuous mode, the sniffer will grab this packet as a legitimate packet and respond accordingly.
  If the suspected host replies to the request, we know that it is in promiscuous mode.
  Clever attackers are of course aware of this and update their sniffers to filter out these packets.
Notes: Demo on ping with ethereal

## Slide 31
ARP Test
  Communications in a LAN rely on the MAC addresses
  ARP request: given the IP address, lookup the MAC address
  In normal scenario, the destination MAC address of the ARP request is the broadcast address (for all machines to receive).
Notes: Demo on ARP with ethereal
To clear ARP entry: arp -d <ip_address>

## Slide 32
  In the ARP test, the administrator sends out an ARP request to the suspect host with all valid information except a bogus destination MAC address.
  A machine that is not in promiscuous mode will ignore the packet.
  If a machine is in promiscuous mode, the ARP request would be accepted and the kernel may process it and reply.

## Slide 33
ICMP Ping Latency Test
  The administrator pings the suspected host and takes the round trip time.
  The administrator then creates a lot of fake TCP connections.
  The sniffer may be processing those packets and the latency will increase.
  The administrator then pings the suspected host again to see if the round trip time is increased.
Notes: ?why he receive the fake TCP conn

## Slide 34: Sniffer Countermeasures
The best countermeasure for a sniffer is to prevent hackers from accessing your systems.
Use switches instead of hubs.
  With a hub, all traffic is shown to each system on the LAN.
  In a switched environment, frames are shown only to the interface where the MAC address actually resides.

## Slide 35
T1
MAC address
aa:aa:aa:aa:aa:aa
T2
MAC address
bb:bb:bb:bb:bb:bb
T3
MAC address
cc:cc:cc:cc:cc:cc
Hub
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
Ignore the frame
No frame received
Accept the frame

## Slide 36
T1
MAC address
aa:aa:aa:aa:aa:aa
Hacker
MAC address
bb:bb:bb:bb:bb:bb
T3
MAC address
cc:cc:cc:cc:cc:cc
Hub
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
Accept the frame
When the NIC is run in promiscuous mode, the frame will be accepted.
No frame received
Notes: Demo on ping using eth0

## Slide 37
T1
MAC address
aa:aa:aa:aa:aa:aa
Hacker
MAC address
bb:bb:bb:bb:bb:bb
T3
MAC address
cc:cc:cc:cc:cc:cc
Switch
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
To
aa:aa:aa:aa:aa:aa
Accept the frame
No frame is received
To
aa:aa:aa:aa:aa:aa
No frame is received
Notes: Demo on ping using eth1

## Slide 38
However, some new sniffers can sniff on switched networks (see later slides).
The best way to avoid damage by sniffers is not to pass usernames and passwords over the network in form of clear text.
  Encryption is the key idea.
  Use SSH instead of telnet.
  Use HTTPS instead of HTTP
  Use SCP and SFTP for file transfer.
Notes: telnet/ssh demo by ethereal
https demo by browser
http/https demo by ethereal

## Slide 39: Advanced Sniffing Techniques
Switch is better than hub, but it is not absolutely secure
  A switch keeps an internal list of the MAC addresses of the hosts that are on its ports.
  Traffic is sent to a port, only if the destination hosts is recorded as being present on that port.
  Attackers have created new methods to get around these technology advancements.

## Slide 40
ARP Flooding
  A switch must keep a table of all MAC addresses appear on each port.
  If a large number of addresses appear on a single port, some switches begin to send all traffic to that port.
    Fail open in repeating mode.

## Slide 41
ARP Spoofing
  It is possible to overwrite the ARP cache on many operating systems.
  It is also possible to associate the hacker’s MAC address with the default gateway’s IP address.
  Cause all outgoing traffic from the target host to be transmitted to the hacker’s host.
  More details in later lectures.
Notes: Show ARP table: arp

## Slide 42
ICMP Redirection
  Change the routing table of the target host.
  The hacker declares himself as the default gateway.
  All outbound traffic from the target host will pass through the hacker’s host.
  The hacker’s host sniffs the traffic and then forwards it to the real gateway so that the target host can still communicate with outside.
  However, the hacker’s host cannot receive return traffic from the real gateway.
  More details in later lectures.
Notes: Show routing table: route

## Slide 43: Reference
Kevin L. Poulsen, “Hack Proofing Your Network: Internet Tradecraft”, Chapter 9, p. 260-284.