## Slide 1: Wireless Security

## Slide 2: Basic Concept of Wireless LAN
WLAN
A type of Local Area Network
Wi-Fi is the implementation of WLAN
Use high frequency Radio Wave (RF)
Speed: 11Mbps to ~11Gbps
Range: 10m (802.11ad) to 5km (802.11y)

## Slide 3
IEEE 802.11 family (See Wiki IEEE 802.11)
  802.11b
    2.4 GHz
    Up to 11Mbps
  802.11a
    5-6 GHz
    Up to 54Mbps
  802.11g
    2.4 GHz
    Up to 54Mbps
  802.11n
    2.4 / 5 GHz
    Up to ~600Mbps

## Slide 4
  802.11ac
    5GHz
    Up to ~1.3Gbps
  802.11ad
    60GHz
    Much shorter range and difficult to pass through obstacles
    Up to ~7Gbps
  802.11ax
    2.4 / 5 GHz
    Up to ~11Gbps

## Slide 5
Channel
  Each frequency range is divided into different channels
  Different countries have different regulations to the allowable channels
Source: http://www.pisa.org.hk/event/wlan_workshop.ppt

## Slide 6
Ad Hoc Mode
  Client to client communication
  Wireless devices can directly communicate with each other
  No access point is needed

## Slide 7
Infrastructure Mode
  Connect to Access Point (AP)
  Most of the wireless networks are connected in this way

## Slide 8
Access Point (AP)
  Serves as a “hub” for wireless clients.
  Bridge between wired and wireless LANs.
Beacon
  A message transmitted at regular intervals by the APs.
  Contain information about the network.
  Used to maintain, to optimize communications, and to automatically connect to the AP.
  Clients can join WLAN by
    Listening to beacon passively, OR
    Sending a probe request and then wait for a probe response.
Notes: Hub: repeat the data packet to ALL connected devices
Switch: only send the data packet to the target device

## Slide 9
SSID (Service Set Identifier)
  Also known as Network Name
  Up to 32 characters
  Usually in form of natural language
BSSID (Basic Service Set Identifier)
  6 bytes in form of a MAC address
BSS (Basic Service Set)
  The set of clients and one AP that have recognized each other and have established communications
ESS (Extended Services Set)
  Series of overlapping BSS connected by a distributed system

## Slide 10
Security Protocols
  Provide security measures such as encryption
  Wired Equivalent Privacy (WEP)
    Broken, can be cracked in few minutes
  Wi-Fi Protected Access (WPA)
    Released in 2003
    Has some security issues (when RC4-TKIP is used)
  Wi-Fi Protected Access II (WPA2)
    Released in 2004
    Most popular nowadays
    More secure than WPA (when AES-CCMP is used)
  Wi-Fi Protected Access 3 (WPA3)
    Released in 2018
    Most secure

## Slide 11: War Driving
Originally, War Driving referred to the case that crackers drove around in a car equipped with wireless gear looking for unsecured wireless networks, to gain illicit access
Nowadays, the term has evolved to include harmless types that simply checking on the WLAN environment

## Slide 12
To perform war driving, we need to have:
  Device capable of
    receiving 802.11 signal
    moving around
  Software that will log data from the device
    Vistumber
    WifiInfoView
Over time, we can build up a database that consists of the network name, the location, the signal strength, the encryption protocol used, etc.

## Slide 13
Professional Information Security Association (PISA) tried her first war driving in Hong Kong in 2002
2002 survey
  187 access points captured
  WEP enable: 22.99%
  WEP disable: 77.01%
Notes: Reference:
http://www.pisa.org.hk/event/wlan_workshop.ppt

## Slide 14
2016 survey
  51,322 access points captured
  With Encryption: 83.68%
    WEP: 3.10%
    WPA: 31.69%
    WPA2: 48.89%
  Without Encryption: 16.32%
Notes: Reference:
http://www.safewifi.hk/files/2017/Report%20on%20Wireless%20LAN%20War%20Driving%20Survey%202016%20Hong%20Kong.pdf
http://dl.aircrack-ng.org/breakingwepandwpa.pdf

## Slide 15: Wireless Router Configuration
Enable WPA3 (for new routers only)
  For current routers, enable WPA2 using AES-CCMP with a strong Pre-Shared Key (PSK)
Disable Wi-Fi Protected Setup (WPS / QSS)
  WPS is a key exchange mechanism providing an easy setup of a Wi-Fi network
  In 2011, a major security flaw was found allowing unauthorized access to the network
  Many old routers have WPS enabled by default, some may even have no option to disable it
  According to PISA in 2016 survey, 33.02% of in the discovered routers still have WPS enabled

## Slide 16
Enable firewall functioning
Make sure that the router's firmware is up-to-date
Enable MAC address filtering
  Only devices with authorized MAC addresses are allowed to connect to the router
  Only avoid unauthorized “normal users” connecting to your WLAN
  Not a reliable security measure against hackers
    Tools can be used to discover the MAC addresses wirelessly
    Hackers can change their MAC addresses accordingly
    Other security measures are still needed

## Slide 17
Network Name Broadcast (Enable / Disable)
  The router broadcasts its network name to nearby client devices regularly
  Hide the SSID = Disable this feature
  There are pros and cons for hiding the SSID
  Pros
    Avoid “normal users” from knowing the existence of the WLAN
    Lower the chance to be targeted by the hackers who want to hack into some “easy-targets”
      The hacker needs to take an extra step to search for hidden networks
      By hiding the network, it at least shows that the network owner knows how to configure the router, where the chance for this router to be set up securely is higher  may not be an “easy-target”

## Slide 18
  Cons
    If your WLAN is already being targeted, it is not a reliable security measure against hackers
    For the client devices, some OSs may broadcast the probe request (that contains the network name) of the hidden network anywhere for them to connect the hidden network
      For example, your mobile phone may broadcast the probe request of your home network even you are in school
      This may cause privacy issues
      But some say that some OSs nowadays broadcast the probe request of a network anywhere no matter whether it is a hidden network or not

## Slide 19: Wired Equivalent Privacy (WEP)
WEP is used in the original 802.11 network to protect link-level data during wireless transmission
  Diagram on the next page
WEP relies on a secret key k shared between the communicating parties

## Slide 20
Application
Transport
(TCP, UDP)
Network (IP)
802.11 Link
Ethernet
Physical
WPA3/WPA2/
WPA/WEP
Network (IP)
802.11 Link
Ethernet
Physical
WPA3/WPA2/
WPA/WEP
Network (IP)
Ethernet
Link
Ethernet
Physical
Application
Transport
(TCP, UDP)
Network (IP)
Ethernet
Link
Ethernet
Physical
Wireless Router
Modified from http://www.pisa.org.hk/event/wlan_workshop.ppt
Client
Server

## Slide 21
Message
Keystream = RC4(IV, k)
Ciphertext
IV
CRC
XOR
Plaintext
Transmitted Data
Initialization Vector (IV)
k: secret key

## Slide 22
Checksumming
  Compute an integrity checksum c(M) on the message M.
  Concatenate the two to obtain a plaintext
  P = <M,c(M)>
Message
CRC
Plaintext

## Slide 23
Encryption
  Choose an Initialization Vector (IV)
    IV must be different for every message transmitted
    802.11 standard doesn't specify how IV is calculated
    Wireless cards use several methods
      Some use a simple ascending counter for each message
      Some switch between alternate ascending and descending counters
      Some use a pseudo random IV generator
  RC4 algorithm generates a keystream: RC4(IV, k)
    Long sequence of pseudorandom bytes
    A function of IV and k
  Exclusive-OR the plaintext with the keystream to obtain the ciphertext C:
Notes: P: 0 0 1 1
RC4(IV,k): 0 1 0 1
C: 0 1 1 0

## Slide 24
Transmission
  Transmit the IV and the ciphertext over the radio link
Decryption
  Get the Initialization Vector (IV)
  Know the shared key k
  RC4 algorithm generates the same keystream: RC4(IV, k)
  Exclusive-OR the ciphertext with the keystream to obtain the plaintext:
  The reverse of exclusive-OR is also exclusive-OR
Notes: P: 0 0 1 1
RC4(IV,k): 0 1 0 1
C: 0 1 1 0

## Slide 25: Weakness of WEP
Invariance weakness
  Existence of a large class of weak keys
  A small part of the secret key determines a large number of bits of the initial permutation
  The patterns resulted from the weak keys propagate into the generated stream
  The occurrences of these patterns can be easily distinguished
  In other words, a small number of weak key bits determine a large number of bits in the output stream

## Slide 26
IV weakness
  Related key vulnerability
  When the same secret part of the key is used with numerous exposed IVs (24-bit only), the attacker can re-derive the secret part by analyzing the key-streams with relatively little work
Open-source implementations of the attack are widely available
  Such as AirSnort and Aircrack-ng
The bottleneck for key recovery is to gather weakly-encrypted frames
Can be cracked in few minutes
Notes:   Reference:
  Scott Fluhrer, Itsik Mantin, and Adi Shamir. Weaknesses in the Key Scheduling Algorithm of RC4. SAC 2001.

## Slide 27: 802.11i
WEP is part of the original 802.11 standard
A new standard 802.11i should be used nowadays
  802.1X Port-Based Network Access Control
    For validation of client and user credentials to prevent unauthorized access to a specified router port
Notes: Reference:
http://tldp.org/HOWTO/html_single/8021X-HOWTO/

## Slide 28
  Encryption
    Temporary Key Integrity Protocol (TKIP)
      Still use RC4 as cryptographic algorithm
      More complex scheme with message authentication, and longer IV (48-bit vs. 24-bit)
      Considered not secure, deprecated in 2012
      Default encryption scheme for WPA
      WPA (with TKIP) is called Transitional Security Network (TSN)
    Counter Mode with CBC-MAC protocol (CCMP)
      Use AES as cryptographic algorithm
      More CPU intensive
      Default encryption scheme for WPA2
      WPA2 (with CCMP) is called Robust Secure Network (RSN)
Notes: Reference:
http://tldp.org/HOWTO/html_single/8021X-HOWTO/

## Slide 29
    WPA/WPA2-PSK
      Pre-shared key / Personal
      The same key among all users
      Suitable for home or small companies
      A strong key should be used to avoid dictionary attack
        At least 12-14 characters containing uppercase letters, lowercase letters, special characters, and digits
    WPA/WPA2-Enterprise
      Different users have different keys
      Authentication server (RADIUS)
Notes: Reference:
http://tldp.org/HOWTO/html_single/8021X-HOWTO/

## Slide 30: Wi-Fi Protected Access II (WPA2)
Image source: Samia Alblwi, Khalil Shujaee. A Survey on Wireless Security Protocol WPA2. SAM17.
Notes: Step 1: The initialization vector (IV), which contains 48-bit replay protection, and the index (KeyID) are used to construct the CCMP header.
Step 2: The CCMP header, session key, and plaintext are used to compute the Message Integrity Code (MIC).
Step 3: IV and plaintext are used to generate the nonce.
Step 4: Plaintext, session key, the MIC, nonce, and the CCMP header are encrypted using AES in order to produce the cipher text.

## Slide 31
Step 1: The initialization vector (IV), which contains 48-bit replay protection, and the index (KeyID) are used to construct the CCMP header.
Step 2: The CCMP header, session key, and plaintext are used to compute the Message Integrity Code (MIC).
Step 3: IV and plaintext are used to generate the nonce.
Step 4: Plaintext, session key, the MIC, nonce, and the CCMP header are encrypted using AES in order to produce the cipher text.

## Slide 32: WPA/WPA2 4-way Handshake
Image Source:. https://www.packtpub.com/books/content/common-wlan-protection-mechanisms-and-their-flaws
Notes: For both parties to know the other one has the correct PSK
  Without sending PSK and PMK out
To generate PTK, which is used to derive the encryption key later
PSK (Pre-shared Key)
PMK (Pairwise Master Key)
  Derived by SSID and PSK using a hash function
A-nonce, S-nonce
  Random integers
PTK (Pairwise Transient Key)
  Derived by PMK, A-nonce, S-nonce, client MAC address, and AP MAC address
  Used for deriving other keys for AES-CCMP / TKIP encryption later

## Slide 33
For both parties to know the other one has the correct PSK
  Without sending PSK and PMK out
To generate PTK, which is used to derive the encryption key later
PSK (Pre-shared Key)
PMK (Pairwise Master Key)
  Derived by SSID and PSK using a hash function
A-nonce, S-nonce
  Random integers
PTK (Pairwise Transient Key)
  Derived by PMK, A-nonce, S-nonce, client MAC address, and AP MAC address
  Used for deriving other keys for AES-CCMP / TKIP encryption later
Notes: Reference:
https://www.packtpub.com/books/content/common-wlan-protection-mechanisms-and-their-flaws
http://etutorials.org/Networking/Wireless+lan+security/Chapter+8.+WLAN+Encryption+and+Data+Integrity+Protocols/Key+Management/

## Slide 34: Attack on WPA / WPA2
Key Reinstallation Attack (KRACK)
  Discovered in 2016
  Man-in-the-middle attack
    Allows decryption, packet replay, TCP connection hijacking, HTTP content injection, etc.
  Affects all major platforms
    Windows, Linux, macOS, Android, iOS, etc.
    Linux and Android affected mostly due to their widely used open-source implementation wpa_supplicant
  Nevertheless, WPA / WPA2 is still more secure than WEP
  Can be fixed by applying patches to OS and routers
Notes: Reference:
https://www.krackattacks.com/

## Slide 35
  Against the 4-way handshake of WPA / WPA2
      After the client receives Message 3, the key will be installed
      The protocol allows Message 3 to be received multiple times
      Each time will reinstall the same encryption key, and reset
        the incremental transmit packet number (nonce)
        receive replay counter
      used by the encryption protocol
  If the same encryption key is used with nonce values that have already been used in the past, the encryption protocols will reuse the previous keystream when encrypting packets
Notes: Reference:
https://www.krackattacks.com/

## Slide 36
  In case a message that reuses keystream has known content, it becomes trivial to derive the used keystream
  In practice, finding packets with known content is not a problem
  This keystream can then be used to decrypt messages with the same nonce
Notes: Reference:
https://www.krackattacks.com/

## Slide 37: Wi-Fi Protected Access 3 (WPA3)
Use Simultaneous Authentication of Equals (SAE) instead of PSK 4-way handshake in WPA/WPA2
  Also known as Dragonfly key exchange
Can prevent Offline Dictionary Attack
  WPA/WPA2 handshake can be captured
  An attacker can perform offline dictionary attack to guess the PSK without any time limitation
Notes: Reference:
https://tools.ietf.org/html/rfc7664
https://spectrum.ieee.org/tech-talk/telecom/security/everything-you-need-to-know-about-wpa3

## Slide 38
Provide Forward Secrecy
  If the key is compromised in one session, the security of earlier sessions will not be affected
  WPA/WPA2 does not provide forward secrecy
    An attacker can store the encrypted traffic first and then decrypt it later after the key is compromised
  SAE provides forward secrecy by generating new keys for different sessions
Provide 192-bit security instead of 128-bit
  For WPA3-Enterprise only
Notes: Reference:
https://tools.ietf.org/html/rfc7664
https://spectrum.ieee.org/tech-talk/telecom/security/everything-you-need-to-know-about-wpa3